## Slide 1: BD Rhapsody™ TCR/BCR Multiomic Assay Unravel the complexity of the adaptive immune system
Notes: To change the images on this slide:
Delete existing image
Drag and drop new image (jpeg or png preferred) into placeholder
Select the new image and “send to back” so that it is behind the masking shape
Change the color of the masking shape to accent the image. Use a color from the Theme Colors

## Slide 2: Overview

## Slide 3
Challenging factors constrain immune profiling
of T and B cell receptor sequences
Diversity of T and B cell repertoires
Analysis at the single-cell level
Sensitive and reproducible methodology
Sequencing limitations for full characterization
Profile the complete V(D)J region of T and B cell molecules at the single-cell level from your cell type of interest alongside a targeted or whole transcriptome mRNA workflow with optional protein profiling using BD® AbSeq Ab-Oligos.
Immune repertoire profiling
Notes: General audience

## Slide 4: Workflow

## Slide 5: BD Rhapsody™ TCR/BCR Multiomic Assay profiling workflow
A continuous ecosystem for high-dimensional biology
BD Vacutainer®
CPT™ Tubes
BD® AbSeq
Ab-Oligos
BD FACS™
Sorters
BD Rhapsody™
System
SeqGeq™
Software
BD FACS™
Analyzers

## Slide 6: BD Rhapsody™ TCR/BCR Multiomic Assay profiling workflow
Perform single-cell partitioning and library prep for simultaneous analysis of gene expression, protein expression and TCR/BCR repertoire with the BD Rhapsody™ Single-Cell Analysis System
BD Rhapsody™ Single-Cell Multiplexing Kit
x12
BD® AbSeq Antibody-Oligonucleotides
BD® AbSeq Single-Vial Reagents, BD® AbSeq Immune Discovery Panel, Custom BD® AbSeq Ab-Oligos
BD Rhapsody™ TCR/BCR
Multiomic Assay Kit
High-parameter full-length
T cell and B cell receptor profiling
In combination with:
BD Rhapsody™ Whole
Transcriptome Analysis Amplification Kit
or
BD Rhapsody™ Targeted mRNA Kit
and AbSeq amplification
BD Rhapsody™ Express System
Single-cell capture, bead-based mRNA isolation and bead retrieval
BD Rhapsody™ System
Single-cell capture, bead-based mRNA isolation and bead retrieval with imaging and cell workflow QC
BD bioinformatics
Sequencing and read alignment
and mapping primary analysis software
SeqGeq™ v1.8 Secondary Analysis
Software for clustering,
visualization and elimination of multiplet data for clean differential expression
Cell staining (optional)
Cell
capture
TCR/BCR
multiomic assay
High-dimensional data analysis

## Slide 7: BD Rhapsody™ TCR/BCR Multiomic Assay for targeted mRNA analysis
cDNA synthesis and template switching
Denaturization and self hybridization
AbSeq/sample tag PCR 1 and cleanup
Extension and exonuclease I treatment
Sample tag library prep
AbSeq library prep
Denature AbSeq/sample tags
Sequence
Sequence
TCR/BCR PCR 1 (on bead)
TCR/BCR library prep
Targeted library prep
Sequence
Sequence
Bioinformatics
Bioinformatics
Bioinformatics
Bioinformatics

## Slide 8: BD Rhapsody™ TCR/BCR Multiomic Assay for whole transcriptome analysis
cDNA synthesis and template switching
Denaturization and self hybridization
AbSeq/sample tag PCR 1 and cleanup
Extension and exonuclease I treatment
Sample tag library prep
AbSeq library prep
Denature AbSeq/sample tags
Sequence
Sequence
WTA random priming and extension (on bead)
TCR/BCR library prep
WTA library prep
Sequence
Sequence
Bioinformatics
Bioinformatics
Bioinformatics
Bioinformatics

## Slide 9: Assay kit

## Slide 10
Full-Length
Assay
High-Quality
Metrics
Deep Sequencing
Not Required
Detection of
Rare Cell Types
3' Gene
Expression
Sample
Multiplexing
Multiomics
Enabled
BD Rhapsody™ TCR/BCR Multiomic Assay

## Slide 11
BD Rhapsody™ TCR/BCR Multiomic Assay
Full-Length
Assay
Uncover clonal diversity of full-length V(D)J sequences for T and B cells at the single-cell level
High-Quality
Metrics
Confidence in data to answer your biological questions
Save on sequencing costs
Recommended sequencing
depth of BCR and TCR libraries
is 5,000 reads per cell

## Slide 12
BD Rhapsody™ TCR/BCR Multiomic Assay
Profile your rare cell types of interest, such as gamma/delta T cells
Compare data across multiple experiments with and without V(D)J
Increase sample throughput and save cost, minimizing batch effects and reduce time to discovery
Detection of
Rare Cell Types
3’ Gene
Expression
Sample
Multiplexing
Easily design your experiments with validated protocols and product while finding everything you need from your trusted partner
Multiomics
Enabled
  The full-length B cell and T cell receptor profiling is compatible with the BD Rhapsody™ System ecosystem of offerings, including:
  BD Rhapsody™ Targeted Amplification Kit using the BD Rhapsody™ Immune Response Panel Hs
  BD Rhapsody™ Whole Transcriptome Analysis Amplification Kit
  BD® Single-Cell Multiplexing Kit
  BD® AbSeq Immune Discovery Panel
  BD® AbSeq Antibody-Oligonucleotides

## Slide 13: Chemistry

## Slide 14
An RNA-based assay for detecting the identity and sequences of T cell receptors and B cell receptors that have many applications including CAR-T therapy, immuno-oncology, immunology, viral infections
Two approaches for studying TCR/BCR
Structure of T cell and B cell receptors
Structure variant alpha: beta, also detects gamma:delta chains
Notes: General audience

## Slide 15
TCR/BCR capture and library preparation
Notes: General audience

## Slide 16
TCR/BCR capture and library preparation
Notes: General audience

## Slide 17
Technical specifications
Specifications: | 
Capture bead | Enhanced bead
Assay compatibility | BD Rhapsody™ Targeted and BD Rhapsody™ WTA Kits (+/- BD® AbSeq Assay/BD® Single-Cell Multiplexing Kit)
PhiX requirement | 3% PhiX (does not apply to TCR/BCR alone or AbSeq/SMK alone)
TCR/BCR sequencing depth | 5,000 reads per cell
Assay time | 2 working days
Cell input | 5,000–20,000 (unless subsampling beads)
AbSeq/SMK library prep | Amplified from supernatant only (not from bead)
Targeted library prep | Amplify TCR/BCR PCR1 first, then go back to beads and amplify targeted mRNA second
WTA library prep | Do WTA RPE on beads first, then go back to beads and amplify TCR/BCR PCR1
Subsampling beads | Yes, for Targeted and WTA workflows but NOT for workflows with AbSeq and SMK
Notes: General audience

## Slide 18: Application performance

## Slide 19: A single workflow profiling TCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched T cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using PBMC cells.
Step 1: Using both protein and gene
expression a user can generate a tSNE
plot and use AbSeq to identify cell
populations
Step 2: An unsupervised phenograph
analysis can be performed for a population of interest

## Slide 20: A single workflow profiling TCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched T cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using PBMC cells.
Step 3: Frequencies of unique clonotypes within separate phenographs can be reported
Step 4: Cells that have the most frequent clonotype can be identified on the tSNE plot

## Slide 21
A single workflow profiling TCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched T cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using PBMC cells.
Cell_Index | Chain_Type | CDR3_Translation_Dominant
54044 | TCR_Alpha | AVLAEGGKLI
54044 | TCR_Beta | ASSLWGSPLH
123296 | TCR_Alpha | AVLAEGGKLI
123296 | TCR_Beta | ASSLWGSPLH
123563 | TCR_Alpha | AVLAEGGKLI
123563 | TCR_Beta | ASSLWGSPLH
147961 | TCR_Alpha | AVLAEGGKLI
147961 | TCR_Beta | ASSLWGSPLH
Step 5: Using AbSeq and WTA information, differential gene and protein expression analysis of cells with the most frequent clonotype vs the rest of the population can be performed
Step 6: Cell IDs and chain information can be obtained from pipeline output files

## Slide 22
A single workflow profiling TCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched T cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using PBMC cells.
Step 7: VDJ and C gene information can be determined for the clonotype of interest
Cell_Index | Chain_Type | V_gene_Dominant | D_gene_Dominant | J_gene_Dominant | C_gene_Dominant | Full_Length | Productive
54044 | TCR_Alpha | TRAV20*01 |  | TRAJ23*01 | TRAC | TRUE | TRUE
54044 | TCR_Beta | TRBV27*01 | TRBD1*01 | TRBJ1-6*02 | TRBC1 | TRUE | TRUE
123296 | TCR_Alpha | TRAV20*01 |  | TRAJ23*01 | TRAC | TRUE | TRUE
123296 | TCR_Beta | TRBV27*01 | TRBD1*01 | TRBJ1-6*02 | TRBC1 | TRUE | TRUE
123563 | TCR_Alpha | TRAV20*01 |  | TRAJ23*01 | TRAC | TRUE | TRUE
123563 | TCR_Beta | TRBV27*01 | TRBD1*01 | TRBJ1-6*02 | TRBC1 | TRUE | TRUE
147961 | TCR_Alpha | TRAV20*01 |  | TRAJ23*01 | TRAC | TRUE | TRUE
147961 | TCR_Beta | TRBV27*01 | TRBD1*01 | TRBJ1-6*02 | TRBC1 | TRUE | TRUE

## Slide 23
A single workflow profiling TCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched T cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using PBMC cells.
Cell_Index | VDJ_Translation_Trimmed
54044 | EDQVTQSPEALRLQEGESSSLNCSYTVSGLRGLFWYRQDPGKGPEFLFTLYSAGEEKEKERLKATLTKKESFLHITAPKPEDSATYLCAVLAEGGKLIFGQGTELSVKP
54044 | EAQVTQNPRYLITVTGKKLTVTCSQNMNHEYMSWYRQDPGLGLRQIYYSMNVEVTDKGDVPEGYKVSRKEKRNFPLILESPSPNQTSLYFCASSLWGSPLHFGNGTRLTVT
123296 | EDQVTQSPEALRLQEGESSSLNCSYTVSGLRGLFWYRQDPGKGPEFLFTLYSAGEEKEKERLKATLTKKESFLHITAPKPEDSATYLCAVLAEGGKLIFGQGTELSVKP
123296 | EAQVTQNPRYLITVTGKKLTVTCSQNMNHEYMSWYRQDPGLGLRQIYYSMNVEVTDKGDVPEGYKVSRKEKRNFPLILESPSPNQTSLYFCASSLWGSPLHFGNGTRLTVT
123563 | EDQVTQSPEALRLQEGESSSLNCSYTVSGLRGLFWYRQDPGKGPEFLFTLYSAGEEKEKERLKATLTKKESFLHITAPKPEDSATYLCAVLAEGGKLIFGQGKELSVKP
123563 | EAQVTQNPRYLITVTGKKLTVTCSQNMNHEYMSWYRQDPGLGLRQIYYSMNVEVTDKGDVPEGYKVSRKEKRNFPLILESPSPNQTSLYFCASSLWGSPLHFGNGTRLTVT
147961 | EDQVTQSPEALRLQEGESSSLNCSYTVSGLRGLFWYRQDPGKGPEFLFTLYSAGEEKEKERLKATLTKKESFLHITAPKPEDSATYLCAVLAEGGKLIFGQGTELSVKP
147961 | EAQVTQNPRYLITVTGKKLTVTCSQNMNHEYMSWYRQDPGLGLRQIYYSMNVEVTDKGDVPEGYKVSRKEKRNFPLILESPSPNQTSLYFCASSLWGSPLHFGNGTRLTVT
TCR_alpha
EDQVTQSPEALRLQEGESSSLNCSYTVSGLRGLFWYRQDPGKGPEFLFTLYSAGEEKEKERLKATLTKKESFLHITAPKPEDSATYLCAVLAEGGKLIFGQGTELSVKP
TCR_beta
EAQVTQNPRYLITVTGKKLTVTCSQNMNHEYMSWYRQDPGLGLRQIYYSMNVEVTDKGDVPEGYKVSRKEKRNFPLILESPSPNQTSLYFCASSLWGSPLHFGNGTRLTVT
Step 8: Full length sequence of clonotype can be obtained (nucleotide sequence also available) VDJ and C gene information can be determined for clonotype of interest
FR1
CDR1
FR2
CDR2
FR3
CDR3
FR4

## Slide 24
A single workflow profiling BCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched B cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using B-enriched cells.
Step 1: Using both protein and gene expression a user can generate a tSNE plot and use AbSeq to identify CD19+ cells
Step 2: An unsupervised phenograph analysis can be performed to identity distinct subgroups within the enriched B cell population

## Slide 25
A single workflow profiling BCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched B cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using B-enriched cells.
Step 3: Using AbSeq WTA information, differential gene and protein expression analysis of two different phenographs can be performed alongside profiling of BCR CDR3 clonotypes
CDR3 clonotypes in phonograph 7
CDR3 clonotypes in phonograph 10

## Slide 26
A single workflow profiling BCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched B cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using B-enriched cells.
Step 4: Clonotypes of interest can be overlayed and identified on a tSNE plot
Step 5: Cell IDs and chain information for clonotypes of interest can be obtained from pipeline output files
Phenograph | CDR3_Translation_Dominant | Cell_Index | Chain_Type | V_gene Dominant | D_gene Dominant | J_gene Dominant | C_gene Dominant | Full_Length | Productive
7 | ARVPNPYGSGSYYKREFDY | 508191 | BCR_Heavy | IGHV4-34*01 | IGHD3-10*01 | IGHJ4*02 | IGHM | TRUE | TRUE
7 | QKYNSAPRT | 508191 | BCR_Kappa | IGKV1-27*01 |  | IGKJ1*01 | IGKC | TRUE | TRUE
10 | AKGTIFGLLNWFDS | 481842 | BCR_Heavy | IGHV3-9*01 | IGHD3-3*01 | IGHJ5*01 | IGHG1 | TRUE | TRUE
10 | QQYGSSPLT | 481842 | BCR_Kappa | IGKV3-20*01 |  | IGKJ4*01 | IGKC | TRUE | TRUE

## Slide 27
A single workflow profiling BCR designed to work alongside Targeted or WTA and protein analysis for multiplexed samples
Resting PBMCs and enriched B cells from different donors were multiplexed and stained with IDP + 4 AbSeq drop-ins and a 15-plex AbSeq panel, respectively. Presented is an example of an analysis using B-enriched cells.
Step 6: Full length sequence of clonotypes can be obtained from pipeline using cell IDs (nucleotide sequence also available)
FR1
CDR1
FR2
CDR2
FR3
CDR3
FR4
Cell_Index | Chain_Type | VDJ_Translation_Trimmed
508191 | BCR_Heavy | QVQLQQWGAGLLKPSETLSLTCAVYGGSFSGYYWSWIRQPPGKGLEWIGEINHSGSTNYNPSLKSRVTISVDTSKNQFSLKLSSVTAADTAVYYCARVPNPYGSGSYYKREFDYWGQGTLVTVSS
508191 | BCR_Kappa | DIQMTQSPSSLSASVGDRVTITCRASQGISNYLAWYQQKPGKVPKLLIYAASTLQSGVPSRFSGSGSGTDFTLTISSLQPEDVATYYCQKYNSAPRTFGQGTKVEIK
502328 | BCR_Heavy | EVQLVESGGGLVQPGRSLRLSCAASGFTFDNFAMHWVRQAPGKGLEWVSGITWNSDTVNYAESVKGRFTISRDNAKNSLYLQMNSLRTEDTAFYYCAKGTIFGLLNWFDSWGQGTLVTVSS
502328 | BCR_Kappa | EIVLTQSPGTLSLSPGERATLSCRASQSFSGSYLAWYQHKPGQAPRLVIYEGSRRATGIPDRFSGSGSGTDFTLTISRLQPEDFAVYNCQQYGSSPLTFGGGTKVEI
BCR_Heavy | QVQLQQWGAGLLKPSETLSLTCAVYGGSFSGYYWSWIRQPPGKGLEWIGEINHSGSTNYNPSLKSRVTISVDTSKNQFSLKLSSVTAADTAVYYCARVPNPYGSGSYYKREFDYWGQGTLVTVSS
BCR_Kappa | DIQMTQSPSSLSASVGDRVTITCRASQGISNYLAWYQQKPGKVPKLLIYAASTLQSGVPSRFSGSGSGTDFTLTISSLQPEDVATYYCQKYNSAPRTFGQGTKVEIK
BCR_Heavy | EVQLVESGGGLVQPGRSLRLSCAASGFTFDNFAMHWVRQAPGKGLEWVSGITWNSDTVNYAESVKGRFTISRDNAKNSLYLQMNSLRTEDTAFYYCAKGTIFGLLNWFDSWGQGTLVTVSS
BCR_Kappa | EIVLTQSPGTLSLSPGERATLSCRASQSFSGSYLAWYQHKPGQAPRLVIYEGSRRATGIPDRFSGSGSGTDFTLTISRLQPEDFAVYNCQQYGSSPLTFGGGTKVEI

## Slide 28
Sequencing and libraries
A high percentage of TCR/BCR sequencing reads that map to reference sequences and a low percentage of reads that are filtered out from the bioinformatics pipeline indicate high-quality sequencing libraries.

## Slide 29: Analysis pipeline

## Slide 30
Sequence analysis pipeline
Inputs
AbSeq references
Reads
Reference genome
Supplemental reference
Transcriptome annotation
App settings
VDJ settings
Cell calling settings
Exact cell count
Putative cell calling
Subsample settings

## Slide 31
Sequence analysis pipeline – TCR/BCR steps
Alignment of TCR and/or BCR reads (to known VDJ gene segments)
Sequestration of reads for specific VDJ processing
Assembly of short reads into longer contigs
QC and error correction
Assessment of contig
Dominant contig is identified for each cell and chain type (e.g., alpha, beta, etc.)
Final error correction
2
1
4
3
5
6
7
Includes
V, D, J, and C segments
CDR1 – 3
FR1 – 4
Productivity
Full length
Protein sequence

## Slide 32
Sequence analysis pipeline files
File Name | Description
Important VDJ Files | 
(runName)_VDJ_perCell.csv | Reports putative cells with their dominant contigs after error correction
(runName)_VDJ_perCell_uncorrected.csv | Reports all cell IDs (putative and non) with uncorrected dominant contigs
(runName)_VDJ_Dominant_Contigs.csv | Reports putative cells and their dominant contig, chain type, nucleotide and amino acid sequence, quality scores, etc.
(runName)_VDJ_Unfiltered_Contigs.csv | Reports all cell IDs with assembled contigs that were annotated
(runName)_VDJ_metrics.csv | TCR/BCR specific metrics file including number of reads aligned, assembled and annotated as well as contig metrics such as percent dominant contigs from a putative cell and mean length of dominant contigs

## Slide 33: Ordering information

## Slide 34
BD Rhapsody™ TCR/BCR Multiomic Assay
To request a quote or place an order, visit bdbiosciences.com, email scomix@bdscomix.bd.com or contact your local BD sales representative.
Assays | Cat. no. | Retail price (USD) 2021
BD Rhapsody™ TCR/BCR Multiomic Assay Kit for Targeted mRNA Analysis* | 665828 | $6,850.00
BD Rhapsody™ TCR/BCR Multiomic Assay Kit for Whole Transcriptome Analysis | 665829 | $6,850.00
Companion products | Cat. no. | Retail price (USD) 2021
BD Rhapsody™ Express Single-Cell Analysis System | 633702 | $0,000.00
BD Rhapsody™ Single-Cell Analysis System | 633707 | $0,000.00
BD® AbSeq Single-Vial Reagents | ─ | $0,000.00
BD® AbSeq Immune Discovery Panel | 625970 | $0,000.00
BD Rhapsody™ Immune Response Panel Hs | 633750 | $0,000.00
BD® Human Single-Cell Multiplexing Kit | 633781 | $0,000.00
Custom BD® AbSeq Ab-Oligos | ─ | $0,000.00
* Targeted panel is required and ordered separately

## Slide 35
Kit contents
Description | Cat. no. | Test/kit
BD Rhapsody™ TCR/BCR Multiomic Assay Kit for Targeted mRNA Analysis |  | 
BD Rhapsody™ Enhanced Cartridge Reagent Kit | 664887 | 4
BD Rhapsody™ Cartridge Kit | 633733 | 4
BD Rhapsody™ TCR/BCR Amplification Kit | 665345 | 4
BD Rhapsody™ Targeted Amplification Kit | 633774 | 4
BD Rhapsody™ cDNA Synthesis Kit | 633773 | 4
Description | Cat. no. | Test/kit
BD Rhapsody™ TCR/BCR Multiomic Assay Kit for Whole Transcriptome Analysis |  | 
BD Rhapsody™ Enhanced Cartridge Reagent Kit | 664887 | 4
BD Rhapsody™ Cartridge Kit | 633733 | 4
BD Rhapsody™ TCR/BCR Amplification Kit | 665345 | 4
BD Rhapsody™ WTA Amplification Kit | 633801 | 4
BD Rhapsody™ cDNA Synthesis Kit | 633773 | 4

## Slide 36
Ancillary components
Material | Supplier | Cat. no.
Reagents |  | 
Agencourt™ AMPure™ XP Magnetic Beads | Major supplier | –
100% ethyl alcohol | Major supplier | –
Nuclease-free water | Major supplier | –
Recommended consumables |  | 
Pipettes (P10, P20, P200, P1000) | Major supplier | –
Low-retention, filtered pipette tips | Major supplier | –
0.2 mL PCR 8-strip tubes | Major supplier | –
15 mL conical tubes | Major supplier | –
DNA LoBind™ Tubes, 1.5 mL | Eppendorf | 0030108051
DNA LoBind™ Tubes, 5.0 mL | Eppendorf | 0030108310
QuBit™ Assay Tubes | Thermo Fisher Scientific | Q32856
Material | Supplier | Cat. no.
Equipment |  | 
Microcentrifuge for 1.5–2.0 mL tubes | Major supplier | –
Microcentrifuge for 0.2 mL tubes | Major supplier | –
Vortexer | Major supplier | –
Digital timer | Major supplier | –
Eppendorf ThermoMixer™ C | Eppendorf | 5382000023
6-tube magnetic separation rack for 1.5 mL tubes | New England Biolabs | S1506S
Low-profile magnetic separation stand for 0.2 mL, 8-strip tubes | V&P Scientific, Inc. | VP772F4-1
QuBit™ 3.0 Fluorometer | Thermo Fisher Scientific | Q33216
Agilent™ 2100 Bioanalyzer Or Agilent™ 4200 TapeStation System | Agilent Technologies | G2940CAG G2991AA

## Slide 37: Available protocols

## Slide 38
BD Rhapsody™ TCR/BCR Multiomic Assay
Targeted-based protocols
BD Rhapsody™ System TCR/BCR full length and targeted mRNA library Preparation Protocol
BD Rhapsody™ System TCR/BCR full length, targeted mRNA and BD® AbSeq Library preparation protocol
BD Rhapsody™ System TCR/BCR full length, targeted mRNA and sample tag library preparation protocol
BD Rhapsody™ System TCR/BCR full length, targeted mRNA and BD® AbSeq and sample tag library preparation protocol
Whole Transcriptome-based protocols
BD Rhapsody™ System TCR/BCR full length and mRNA whole transcriptome analysis (WTA) library preparation protocol
BD Rhapsody™ System TCR/BCR full length, mRNA whole transcriptome analysis (WTA) and BD® AbSeq Library preparation protocol
BD Rhapsody™ System TCR/BCR full length, mRNA whole transcriptome analysis (WTA) and sample tag library preparation protocol
BD Rhapsody™ System TCR/BCR full length, mRNA whole transcriptome analysis (WTA) and BD® AbSeq and sample tag library preparation protocol

## Slide 39: Sequencing recommendations

## Slide 40
Read requirements for sample tags/AbSeq and targeted mRNA analysis
Gene panel | Read requirement for data analysis | Adjusted reads for sequencing pooled TCR/BCR libraries on Illumina™ platforms*
BD Rhapsody™ Immune Response Panel Hs | ~2,000–20,000 reads/cell* | N/A
Sample tag: samples from same type of cell (combining different donor PBMCs) | 120 reads/cell | N/A
Sample tag: samples from same type of cell (combining different type of cell line with PBMCs) | 600 reads/cell | N/A
BD® AbSeq Panel | 1,000 reads/cell/AbSeq* | N/A
BD Rhapsody™ TCR Panel | ~5,000 reads/T cell | ~15,000 reads/T cell*
BD Rhapsody™ BCR Panel | ~5,000 reads/B cell | ~15,000 reads/B cell*
*See protocols for more detailed sequencing recommendations

## Slide 41
Read requirements for sample tags/AbSeq and whole transcriptome analysis
Gene panel | Read requirement for data analysis | Adjusted reads for sequencing pooled TCR/BCR libraries on Illumina™ platforms*
BD Rhapsody™ Immune Response Panel Hs | ~2,000–20,000 reads/cell* | N/A
Sample tag: samples from same type of cell (combining different donor PBMCs) | 120 reads/cell | N/A
Sample tag: samples from same type of cell (combining different type of cell line with PBMCs) | 600 reads/cell | N/A
BD® AbSeq Panel | 1,000 reads/cell/AbSeq* | N/A
BD Rhapsody™ TCR Panel | ~5,000 reads/T cell | ~25,000 reads/T cell*
BD Rhapsody™ BCR Panel | ~5,000 reads/B cell | ~25,000 reads/B cell*
*See protocols for more detailed sequencing recommendations
Sequence AbSeq libraries together (recommended) or separately from sample tag, WTA and TCR/BCR libraires
WTA Library
10,000 reads/cell for shallow sequencing
50,000 reads/cell for moderate sequencing
100,000 reads/cell for highly saturated deep sequencing

## Slide 42
Example of pooling AbSeq/sample tag using enriched T or B cells or PBMCs stained with 30-plex BD® AbSeq Panel
Library type | Reads/cell | Correction factor for low clustering | Cell number | Reads needed | % pooling | Volume based on total 50 µL pool
Calculating pooling rations based on 10,000 T or B cells or 10,000 PBMCs |  |  |  |  |  | 
ST (combining different cell types) | 600 | N/A | 10,000 | 6,000,000 | 2% | 1 µL
AbSeq 30-plex | 300,000 | N/A | 10,000 | 300,000,000 | 98% | 49 µL
Total |  |  |  | 300,000,000 | 100% | 50 µL
Sequenced separately

## Slide 43
Example of pooling targeted mRNA and TCR/BCR libraries from enriched T or B cells
Sequenced separately
Library type | Reads/cell | Correction factor for low clustering | Cell number | Reads needed | % pooling | Volume based on total 50 µL pool
Calculating pooling rations based on 10,000 T or B cells |  |  |  |  |  | 
mRNA targeted | 2,000 | N/A | 10,000 | 20,000,000 | 12% | 6 µL
TCR or BCR | 5,000 | 3 | 10,000 | 150,000,000 | 88% | 44 µL
Total |  |  |  | 170,000,000 | 100% | 50 µL

## Slide 44
Example of pooling targeted mRNA and TCR/BCR libraries from PBMCs
Sequenced separately
Library type | Reads/cell | Correction factor for low clustering | Cell number | Reads needed | % pooling | Volume based on total 50 µL pool
Calculating pooling rations based on 10,000 PBMCs, assuming 20% B cells and 40% T cells in the PBMC population |  |  |  |  |  | 
mRNA targeted | 2,000 | N/A | 10,000 | 20,000,000 | 18% | 9.1 µL
TCR | 5,000 | 3 | 4,000 | 60,000,000 | 55% | 27.3 µL
BCR | 5,000 | 3 | 2,000 | 30,000,000 | 27% | 13.6 µL
Total |  |  |  | 110,000,000 | 100% | 50 µL

## Slide 45
Example of pooling using enriched T or B Cells stained with 30-plex BD® AbSeq Panel
Sequenced in combination with other libraries
Library type | Reads/cell | Correction factor for low clustering | Cell number | Reads needed | % pooling | Volume based on total 50 µL pool
Calculating pooling rations based on 10,000 T or B cells |  |  |  |  |  | 
mRNA targeted | 2,000 | N/A | 10,000 | 20,000,000 | 4% | 2.5 µL
ST (combining different cell types | 600 | N/A | 10,000 | 6,000,000 | 1% | 0.8 µL
AbSeq 30-plex | 30,000 | N/A | 10,000 | 300,000,000 | 63% | 37.8 µL
TCR or BCR | 5,000 | 3 | 10,000 | 150,000,000 | 32% | 18.9µL
Total |  |  |  | 476,000,000 | 100% | 60µL

## Slide 46
Example of pooling using PBMCs stained with 30-plex BD® AbSeq Panel
Sequenced in combination with other libraries
Library type | Reads/cell | Correction factor for low clustering | Cell number | Reads needed | % pooling | Volume based on total 50 µL pool
Calculating pooling rations based on 10,000 PBMCs, assuming 20% B cells and 40% T cells in the PBMC population |  |  |  |  |  | 
mRNA targeted | 2,000 | N/A | 10,000 | 20,000,000 | 4.8% | 2.9 µL
ST (combining different cell types | 600 | N/A | 10,000 | 6,000,000 | 1.4% | 0.9 µL
AbSeq 30-plex | 30,000 | N/A | 10,000 | 300,000,000 | 72.1% | 43.3 µL
TCR | 5,000 | 3 | 4,000 | 60,000,000 | 14.4% | 8.7 µL
BCR | 5,000 | 3 | 2,000 | 30,000,000 | 7.2% | 4.3 µL
Total |  |  |  | 416,000,000 | 100% | 60 µL

## Slide 47
AbSeq/sample tag libraries
Parameter | Requirement
Platform | Illumina: 150 cycle kit
Paired-end reads | Minimum of 51 x 75 read length
PhiX | Required (15%)
Analysis | See the BD® Single-Cell Multiomics Bioinformatics Handbook (Doc ID: 54169)
Calculate the molar concentration of targeted mRNA, sample tag, AbSeq and TCR/BCR libraries using Qubit quantitation concentration (ng/µL) and average BioAnalyzer size (200–1000 bp)
For TCR/BCR libraries, the expected Qubit concentration should be >1.5 ng/µL
Use the calculated molar concentrations to pool libraries
For NextSeq™ and MiniSeq™ High or Mid Output runs, load the flow cell:
Concentration between 1.8–2.2 pM
15% PhiX

## Slide 48
Sequencing flow cell loading and PhiX concentrations
AbSeq/sample tag libraries
Parameter | Requirement
Platform | Illumina: 150 cycle kit
Paired-end reads | Minimum of 51 x 75 read length
PhiX | Required (15%)
Analysis | See the BD® Single-Cell Multiomics Bioinformatics Handbook (Doc ID: 54169)
Calculate the molar concentration of targeted mRNA, sample tag, AbSeq, and TCR/BCR libraries using Qubit quantitation concentration (ng/µL) and average BioAnalyzer size (200–1000 bp)
For TCR/BCR libraries, the expected Qubit concentration should be >1.5 ng/µL
Use the calculated molar concentrations to pool libraries
For NextSeq™ and MiniSeq™ High or Mid Output runs, load the flow cell:
Concentration between 1.8–2.2 pM
15% PhiX

## Slide 49
Sequencing flow cell loading and PhiX Concentrations targeted mRNA and TCR/BCR Libraries (with and without AbSeq)
Parameter | Requirement
Platform | Illumina: 300 cycle kit
Paired-end reads | Minimum of 85 x 215* read length
PhiX | Required (3%)
Analysis | See the BD® Single-Cell Multiomics Bioinformatics Handbook (Doc ID: 54169)
Calculate the molar concentration of targeted mRNA, sample tag, AbSeq, and TCR/BCR libraries using Qubit quantitation concentration (ng/µL) and average BioAnalyzer size (200–1000 bp)
For TCR/BCR libraries, the expected Qubit concentration should be >1.5 ng/µL
Use the calculated molar concentrations to pool libraries
*See protocols for more detailed sequencing recommendations
For NextSeq™ and MiniSeq™ High or Mid Output runs, load the flow cell:
Concentration between 1.8–2.2 pM
15% PhiX
Illumina™ BaseSpace™:
Enter pooled libraries as one sample if libraries were made with the same library forward primer but different indices

## Slide 50
Utilize our expertise and insights for your single cell experiments.
Reach out to your local BD sales representative or contact our help desk scomix@bdscomix.bd.com to learn more about using the BD Rhapsody™ TCR/BCR Multiomic Assay
Support
BD Rhapsody™ TCR/BCR Multiomic Assay

## Slide 51: Thank You
For Research Use Only. Not for use in diagnostic or therapeutic procedures.
BD, the BD Logo, CPT, FACS, Rhapsody, SeqGeq and Vacutainer are trademarks of Becton, Dickinson and Company or its affiliates. All other trademarks are the property of their respective owners. © 2022 BD. All rights reserved. BD-53198 (v1.0) 0222